## Slide 1
BAR – Inflatable Blade
Nicole Mendoza, Ph.D.

## Slide 2: Inflatable Blade Concept
Legend
Foam filler
Uniaxial CF
Air
foam-filled section
(hard, rigid)
exterior Kevlar only
soaked with Teflon
Aero shell created with 2 layers of Kevlar with filler in between
pre-made pultruded uniaxial CF pre-inserted into pocket
pre-sewn compartment structure
design can support both rounded and sharp SSTE
PSTE must be rigid (foam)
to attach TE devices
air-filled sections allow for shape control &
pneumatic actuation (can also sew in air tubes)
*** could have spanwise compartments to pneumatically actuate to stall! ***
traditionally-constructed
primary structure (box beam, double web, etc.)
Materials
Kevlar – reliable (military, re-entry grade), non-conducting (lightening), flame resistant (seams and thread done same as parachutes)
Teflon – protects Kevlar from UV, mitigates icing and soiling, white (soaked)
Foam – lightweight, rigid  maintains aerodynamic shape
Uniaxial CF – provides strength for buckling

## Slide 3: Inflatable Blade Concept
Factory
Fabric/textile manufacturing executed in parallel with primary structure manufacturing (traditional), then joined during curing phase, then shipped
Transportation
Transport by train, deflated and attached (smaller in chord, lighter)
On-site Manufacturing
Inflate mandrels
Inject foam  let harden
Deflate & remove mandrels
Glue on LEP, passive aero devices
Smooth/putty over injection ports (no need to paint blade)
Legend
Foam filler
Uniaxial CF
Air
could insert mandrels here
foam-filled section
(hard, rigid)
exterior Kevlar only
soaked with Teflon
Aero shell created with 2 layers of Kevlar with filler in between
pre-made pultruded uniaxial CF pre-inserted into pocket
pre-sewn compartment structure
design can support both rounded and sharp SSTE
PSTE must be rigid (foam)
to attach TE devices
air-filled sections allow for shape control &
pneumatic actuation (can also sew in air tubes)
*** could have spanwise compartments to pneumatically actuate to stall! ***
traditionally-constructed
primary structure (box beam, double web, etc.)

## Slide 4: Inflatable Blade Concept
Unknowns/Issues
How thin can get outboard TE? (  minimum thickness of 2 Kevlar layers)
How to glue add-ons to Teflon? (  avoid soaking those areas, use seams)
Possible failure mode is delamination of Teflon-coated Kevlar to foam
Flap/edge/torsional stiffnesses?
Features
Re-usable primary structure facilitates derivative blade products (within 2 aero-structural constraints)
Air-filled compartments yield pneumatic aero shape control (airfoil shape and pitch/stall control)
No pressurized air (unless have pneumatically actuated compartments), so won't “burst” under extreme conditions
Compartmental design can easily be segmented/compartmentalized spanwise and chordwise via sewing seams – any size, any #
This concept does not consider structural spanwise segmenting (joints)  other BAR task
Legend
Foam filler
Uniaxial CF
Air
foam-filled section
(hard, rigid)
exterior Kevlar only
soaked with Teflon
Aero shell created with 2 layers of Kevlar with filler in between
pre-made pultruded uniaxial CF pre-inserted into pocket
pre-sewn compartment structure
design can support both rounded and sharp SSTE
PSTE must be rigid (foam)
to attach TE devices
air-filled sections allow for shape control &
pneumatic actuation (can also sew in air tubes)
*** could have spanwise compartments to pneumatically actuate to stall! ***
traditionally-constructed
primary structure (box beam, double web, etc.)

## Slide 5: Design Considerations
Attachment Mechanism (Shell to Structure)
Include 2 Kevlar layers (minimum) in top and bottom of primary structure inside mold @ SS/PS max thk pos before curing
  would need new molds anyways (smaller, lighter)
Cure primary structure + Kevlar layers, remove from molds
Sew/join Kevlar shell to dry Kevlar on primary structure
Design supports both traditional and filament-wound primary structures
Aft Panel Spar Caps / Side Beam
Designs fully supports addition with no restrictions
Simply create compartment and fill with rigid foam
Will need another mandrel for internal aft section
Peel Ply
Vacuum Bag
Kevlar
Tacky Tape
mold
shear web
CF spar cap/beam
Note: Drawings NOT TO SCALE
Example of Chordwise and Spanwise Compartmentalization
Aero-Structure Coupling
Reusability of primary structure to create derivative blades is subject to two design restrictions/constraints
  Airfoil families (geometry)
  Blade absolute thickness spanwise distribution
Most likely structure will constrain aero (will have some wiggle room)
PS max thk pos & value
SS max thk pos & value
Airfoil max thk pos & value

## Slide 6: Design Considerations
Exterior Shape Control
Option # 1 Option # 2 Option # 3
Station Templates Traditional Mold 3D-Printed Segments
Price: $ (or less)
Can be made in parallel to or before blade manufacturing (laser cut)
Easily storable (low space required)
Recyclable
Any # along span (20-25?)
Split @ LE, TE mold release lines
Least/smallest amount of shape control
Most likely wood or recycled plastic
On-site usage (easily transported)
Interchangeable for new blades
Price: $$
Create traditional mold using standard methods
Need to transport to site (large, lighter)
Make prior to blade manufacturing
Must have injection ports
Most/highest amount of shape control
Not reusable/recyclable
Split @ LE, TE mold release lines
Need supporting equipment (cranes, etc.)
?
Price: ? = OPEX (segments) + CAPEX (machine)
Any # of variably-sized spanwise blade segments  variable amount of shape control
Depends on University of Maine printer: 30m X 6.7m X 3m (L X W X H)
Easily segmentable and transportable
Use recyclable materials (wood cellulose and/or recycled plastic)
Split @ LE, TE mold release lines
Can be made in parallel to or before blade manufacturing

## Slide 7: Design Challenges
Problem/Challenge | Proposed Solution
Flap/edge/torsional stiffness | ?
Attachment/loads transfer | Include Kevlar layers in primary structure curing process
Buckling | Pre-made, pre-inserted uniaxial CF
Material reliability / O&M costs | Kevlar, Teflon coating
Aero shape/performance/airfoils | Rigid foam
Aeroelasticity/aeroacoustics/wake | Rigid foam
Controls | Neutral; Would simplify pitch system & give more control authority if use active air devices
Transport/logistics/installation | Easier due to reduced chord and weight
Rest of turbine design | Minimally affected (easier due to reduced weight)
Primary design benefits:
Reduced mass/weight
Reduced chord during transportation  no maximum chord constraint!
Design supports all structural and aerodynamic needs of all OEMs

## Slide 8: Project Plan
| Mar | Apr | May | Jun | Jul | Aug | Sept | Oct | Nov | Dec
Industry AB Mtg
Industry AB Mtg
FY20 Reports Due
AIAA SciTech abstracts due
Sandia Blade Workshop
Go/No-Go
Steps 0, ½, 1a)-1x)
1 cross-section
Resources:
Roland: ~20% time
Nicole: ~12 hrs/month
1 Cross-section:
Steps 2,3
Multiple stations (blade)
openFAST (& LCOE) calcs
New blade designs
Tech Reports & documentation
Journal & conference papers